## Slide 1: Project Milestone 3 Presentation
Course: ENGR 413 | AI in Engineering | Fall 2025
Team Members:
Kavin Krishnakumar (924296929),
Ratchagan Pandiyan (924369976)

## Slide 2: Introduction (Real-World Motivation)
The Need for Smart Energy Scheduling
Residential electricity demand is increasing due to EV charging, HVAC systems, and appliances.
Power utilities use Time-of-Use (TOU) pricing, where electricity costs vary by hour.
Households often operate appliances without considering price changes → higher electricity bills.
Manual scheduling is impractical because:
  User habits vary.
  Appliances have constraints (windows, durations, sequences).
  Cost optimization depends on future load.

## Slide 3: Problem Definition
Goal
Create an intelligent energy management system that:
Predicts household electricity demand.
Uses the prediction to optimally schedule appliances.
Minimizes electricity bills while satisfying real-world constraints.
Why This Problem Matters
Reduces energy waste.
Saves cost under TOU pricing.
Prepares households for smart grid integration and demand response.

## Slide 4: Project Objectives & Scope
Objectives
Build a forecasting model (LSTM) to predict the next 24 hours of aggregate power.
Develop a scheduling optimizer (MILP) that uses the forecast to minimize cost.
Include realistic constraints (power cap, precedence, allowed windows).
Evaluate savings, peak demand, and system feasibility.
Scope
Dataset: UK-DALE House 1.
Appliances modeled: Washer, Dryer, EV Charging.
Scheduling horizon: 24 hours.
TOU tariff and user-defined constraints.

## Slide 5: Background & Related Work
Prior Literature Findings
LSTM networks outperform classical models (ARIMA, linear regression) in electricity forecasting due to their ability to capture long-term dependencies.
Household scheduling research typically uses:
  Heuristics (shift to cheapest hour)
  Genetic algorithms
  Basic rule-based systems → But these do not guarantee optimality.
Gap
Few works directly combine deep learning forecasts with MILP optimization for a fully automated energy management system.

## Slide 6: Dataset Description (UK-DALE)
Dataset Summary
Source: UK Domestic Appliance-Level Electricity dataset (public).
House 1: ~1-year worth of power data at 1-minute resolution.
Columns used:
  timestamp
  aggregate power (Watts)
Preprocessing
Converted timestamp → datetime.
Handled missing values by interpolation.
Converted Watts → kW for cost computation.
Extracted time features: hour, day of week, month.
Sorted chronologically.

## Slide 7: Data Splitting & Normalization
Data Split
Train: 60%
Validation: 20%
Test: 20%
Split controlled by date indices.
Scaling
StandardScaler fitted only on training features.
Prevents data leakage.
Same scaler reused during inference.
Artifacts Saved
scaler.pkl
train_idx.csv, val_idx.csv, test_idx.csv

## Slide 8: System Pipeline (Workflow Diagram)
Raw Data
Train LSTM Forecast Model
Compute KPIs (Cost, Peak, Savings)
MILP Optimization
Predict Next 24 Hours
Generate Appliance Schedule
Preprocessing & Scaling
Why This Pipeline
Splits forecasting and scheduling (modular).
Allows the scheduler to work with any demand prediction model.

## Slide 9: LSTM Model Architecture
Model Details
Input window: 168 hours (7 days).
Output horizon: 24 hours.
Architecture:
  1 × LSTM Layer (64 hidden units)
  Dense layer → 24 outputs
Loss: MSE
Optimizer: Adam (lr = 0.001)
Batch size: 64
Epochs: 20
Framework: PyTorch
Why LSTM?
Captures temporal patterns in daily energy usage.
Handles seasonality (weekday/weekend cycles).

## Slide 10: Project Directory Structure

## Slide 11: Forecast Example (Model Output)
LSTM 24-h Prediction vs Actual
Interpretation
Forecast follows daily trend (morning peaks, evening spikes).
Acceptable error margin for scheduling tasks.
Good enough for downstream MILP optimization.

## Slide 12: MILP Scheduler (Formulation)
Optimization Goal
Minimize:
Total Cost = Σ (Price[h] × (BaseLoad[h] + ApplianceLoad[h]))
Constraints
Power Cap: Total load ≤ 5 kW per hour.
Precedence: Washer must finish before Dryer.
Allowed Windows:
  EV → 0:00–08:00
  Washer → 07:00–22:00
  Dryer → 08:00–23:00
Duration:
  EV needs 4 hours
  Washer 1 hour
  Dryer 1 hour
Why MILP?
Guarantees optimal solution.
Transparent constraint modeling.

## Slide 13: Optimized Schedule (Gantt Chart)
What the Gantt Chart Shows
EV charging shifted to cheapest off-peak hours.
Washer scheduled early evening.
Dryer starts only after Washer finishes (precedence satisfied).
All operations kept under 5 kW cap.

## Slide 14: KPI Comparison (Charts & Table)
Key Results
Naive cost: $2.80
MILP cost: $2.67
Savings: $0.132 (≈ 5%)
Peak demand: unchanged (within limit)
Constraints: fully satisfied

## Slide 15: Discussion & Limitations
Findings
LSTM effectively predicts daily shape of demand.
MILP optimizer enforces realistic constraints and shifts large loads to cheaper hours.
Demonstrated measurable cost savings.
Limitations
Dataset from a single household (House 1 only).
LSTM could be improved with rolling statistics.
Savings depend heavily on TOU price spread.
No renewable energy integration (solar PV).

## Slide 16: Conclusion
Contributions
Built a complete AI pipeline: forecast → optimize → evaluate.
Implemented LSTM + MILP for smart home energy management.
Showed real cost savings and power-limit compliance.
Reproducible via scripts and artifacts.

## Slide 17: Future Work
Next Steps
Add rolling mean, lag-24, and anomaly features.
Evaluate multiple households and compare accuracy.
Simulate different tariff models (flat, real-time prices).
Add solar generation and storage (battery).
Deploy interactive dashboard (Streamlit or Dash).

## Slide 18: Q&A